Configuring Remote Access to MySQL Databases

In order to be able to connect to a remote MySQL server, some setup is required.

Creating the Users

You will need to create user(s) on the remote server with the necessary permissions. The client will log in using on of these users.

To create a user:

create user 'some_user_name'@'localhost' identified by ‘some_password';
create user ‘some_user_name'@'%' identified by 'some_password';

To grant the permissions:

grant all on *.* to 'some_user_name'@'localhost' with grant option;
grant all on *.* to ‘some_user_name'@'%' with grant option;

I created the following users for this purpose:

+----------+---------------+-----------+
| computer | user | host |
+----------+---------------+-----------+
| thinkpad | imac | % |
| thinkpad | imac | localhost |
| thinkpad | root | localhost |
| imac | imac | % |
| imac | imac | localhost |
| imac | root | localhost |
+----------+---------------+-----------+

Connecting to the Remote MySQL Server

To connect from the iMac to a remote MySQL Server running on the ThinkPad, enter the following in the terminal on the iMac:

mysql -u thinkpad -p -h ip_address_of_thinkpad

Similarly, to connect from the ThinkPad to a remote server running on the iMac, enter the following in the terminal on the ThinkPad:

mysql -u imac -p -h ip_address_of_imac

Configuring the Bind Address

You may get the following error when trying to connect:

ERROR 2003 (HY000): Can't connect to MySQL server on '192.168.0.134' (61)

To resolve this, add the following the the appropriate configuration file in the [mysqld] section:

bind-address=0.0.0.0

Computer	Pathname of Configuration File
iMac	/etc/my.cnf
ThinkPad	/etc/mysql/mysql.conf.d/mysqld.cnf

The pathname of your configuration file may be different; it varies based on the operating system. The value used is shown on the Server Status page in MySQL Workbench.

You will need to restart the server after editing these files.